## Slide 1
Tip cleaning: UV ozone
Imaged before UV ozone cleaning
Imaged w. better tip (same day)
After cleaning (and 5 days later)
It seems it does work a bit at least.
Procedure used:
Rinse tip in ethanol.
In UV ozone cleaner for 10 minutes
  (8th floor room 828, contact person Rob Zondervan)
Rinse with ethanol again
N dry.
I suspect that it is the last ethanol rinse that is important
Sample is MBL/MASP complexes. It seems we only see MASPs.
The density is probably very low due to a rinse with buffer before DI water rinsing.
Perhaps complexes sedimented due to 6 min ultracentrifugation or they wre washed of.
Henriette October 15 2002.